## Slide 1: ROBOT DESIGN LESSON
Gearing For LEGO Robots

## Slide 2: Objectives
Learn about the different types of LEGO gears and what you use them for
Learn how to calculate gear ratios
Learn some useful gearing techniques

## Slide 3: What Is a Gear?
A gear is a wheel with teeth that meshes with another gear
There are many different kinds of gears
Gears are used to
  Change speed
  Change torque
  Change direction

## Slide 4: COMMON LEGO GEARS
Turntable
Worm Gear
Rack Gear
Spur Gears
Double Bevel Gears
Single Bevel Gears
Knob Wheel
Crown Gear
Differential

## Slide 5: Naming LEGO GEARS
LEGO gears are referred to by their type and the number of teeth they have
8 tooth spur gear
16 tooth spur gear
24 tooth spur gear
40 tooth spur gear

## Slide 6: Drivers, Followers & Idlers
Driver: gear that applies force (the gear connected to the motor on a robot)
Follower: final gear that is driven
Idler: gear turned by driver which then turns the follower
Notes about gears:
1) When 2 gears mesh, the driver makes follower turn in the opposite direction
2) You need an odd number of idler gears to make driver and follower turn in same direction.
3) You need an even number of idlers (or none) to make driver and follower turn in opposite direction
Driver
Follower
Idler
Idler
Idler

## Slide 7: Gearing Down and Up
Large Driver
Small Follower
Small Driver
Large Follower
Gearing Down
(increases torque, decreases speed)
Gearing Up
(increases speed, decreases torque)
Drive
Drive

## Slide 8: Calculating Gear Ratios
Gear Ratio = number of teeth in follower: number of teeth in driver
Driver
Follower
Driver
Follower
24/40 = 3:5
40/24 = 5:3
Gearing Down
(increases torque, decreases speed)
Gearing Up
(increases speed, decreases torque)

## Slide 9: Change the Direction of Motion
You can use gears to change the direction of motion.
Credits: All the animated images are from: http://technicopedia.com/fundamentals.html. To view them correctly, you will need to use “Slideshow Mode” on PowerPoint.

## Slide 10: PROBLEMS with LEGO gears
Two common problems that you might face:
  Gear Slip: Slippage is when the teeth skip on the gears when you apply power
  Gear Backlash: Backlash is space between the teeth where the gears mesh. When the space is too much, it is called slack/slop. When there is too little, you create too much friction.
Solution: Try to avoid long sequences of gears. Use a gear box. Mesh gears according to specification.

## Slide 11: Gear boxes Can be helpful
Gear boxes can help reduce some of the issues you may face when building with gears.
Some are pre-built (with gears included)
Some need gears inserted into a gear box
Some can be assembled from scratch using technic pieces
Pre-built
Pre-built
Pre-built

## Slide 12: RACK GEARS For Vertical & Horizontal Movement
Support structure of Wall-E7 by Marc-Andre Bazergui is made with rack gears
PIX3L PLOTT3R by Sanjay and Arvind Seshan uses rack gears

## Slide 13: USEFUL ONLINE GEAR TOOL
http://gears.sariel.pl/

## Slide 14: OTHER Useful resources
More about gears: http://sariel.pl/2009/09/gears-tutorial/
Gear animations: http://technicopedia.com/fundamentals.html
Technic Gearing: Books by Yoshihito Isogawa

## Slide 15: Credits
This tutorial was created by Sanjay Seshan and Arvind Seshan
More lessons at www.ev3lessons.com and www.flltutorials.com
This work is licensed under a Creative Commons Attribution-NonCommercial-ShareAlike 4.0 International License.